## Slide 1: Eddy Covariance Data Processing
Hydromet Research Group

## Slide 2: Overview
Data Types
Data Prep
Data Cleaning/filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 3: Data Types
Raw Data Types:
  Processed on the logger (30 Min output)
  Raw High-Frequency Data (10hz or 20hz)
Sensor Types:
  Open
  Closed
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 4: Data Prep
Process high-frequency fluxes into 30min values (if done on the logger ignore) [Appendix 1 for typical corrections]
  Licor: EddyPro (https://www.licor.com/env/products/eddy_covariance/eddypro)
  Campbell Scientific: EasyFlux (https://www.campbellsci.cc/easyflux-pc)
  Custom code
Standardize (Recommend doing this in Excel)
  Variable units
  Variables
  Ranges
  Dates (Appendix 2 for code)
  Na values
Correct (gap fill for major losses based on relations if possible usually use an r2>0.8)
Check
  Data Completeness
  Reasonable ranges
  Expected trends
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 5: Data Prep
Variables that we include at the minimum:
  NEE
  Qe
  Qh
  Tair
  Rh
  Tsoil (Not always needed)
  Qg
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE
  Qnet
  Pressure
  WS
  WD
  SigmaV
  Ustar (U*)
  Rg
  Number of Samples

## Slide 6: Data Cleaning/Filtering
Work in R from now on
Filter for reasonable values (remove large outliers)
Filter for:
  Sufficient number of samples in the 30min time block (18000, 36000 for 10hz, 20hz, respectively) n>85%
  If open path system, remove periods or precip or when air temp < dewpoint temp as there is the potential for moisture on the lens.
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 7: Data Cleaning/Filtering
Roll Apply (NEE, Qh, Qe)
  Compute mean and SD for +- 5 half hours (if 80% of samples are present) and check to see if the value is within +-3.5 SD if not remove
  If there are not enough samples, try to compute mean and SD for +- 10 half hours (if 80% of samples are present) and check to see if the value is within +-3.5 SD if not remove
  If there are not enough samples remove the point
3.5 SD Year and if outside of the range, remove
3.5 SD hours per year and if outside of the range, remove
Manual yearly check to remove values
Manual hour check to remove values
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 8: Data Checking
Check all data as there are many things and potentially other things occurring in the data.
  Biggest things to check are the fluxes (NEE, Qh, Qe)
  Wind direction
  Tair
  Rh
  Qg
  Tsoil
  Qnet
  Incoming radiation (global or PAR)
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 9: Footprinting
Klujn footprinting method (https://footprint.kljun.net/)
  Two Scripts (R; Python; Matlab):
    calc_footprint_FFP (calculates footprint for each half-hour (or timestep))
      Gets distances from which you can filter out the fluxes (we use distance away from tower at the 80% flux for [N, NE, E, SE, S, SW, W, NW])
        To estimate distances available for us we just use measuring on google earth.
    calc_footprint_FFP_climatology (computes area graphs)
      After filtering out the fluxes, use the subset in this to get the images of the flux footprints for creating maps.
        Any real subset (recommend that it is filtered first) can be put into here so its pretty flexible (Time of year or something)
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 10: U* Threshold
Use a static (we use 0.1 m/s) (any U* below this value gets removed)
Can derive it based on site values (Respiration vs U*), and this can be done for each year or seasonally (important for full-year data)
  https://www.bgc-jena.mpg.de/bgi/index.php/Services/REddyProcWeb
    This is an R Package (REddyProc) that can be used for (Wutzler et al., 2018):
      Gapfilling (Met values and fluxes)
      U* threshold calculation
      Carbon Partitioning
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 11: Carbon Partitioning
We use the REddyProc package to partition our NEE into Ecosystem Respiration and GPP
  Creates a regression based on air temp or Soil temp (I find air temp works much better) and night-time NEE (Respiration) and then scales that up for the day. And the GPP is derived from the difference.
  This method also gapfills fluxes, and the corresponding met values needed for the partitioning of the NEE (Rg, temp value (air or soil), U*, VPD).
  Many other methods are possible with this package, but we use the default partitioning method.
  (follow package vignettes for examples)
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 12: Energy Fluxes
Many methods for calculating the heat fluxes, and this depends on what you are trying to do.
Energy Balance Options
  Unclosed
  Closed (Remaining energy is divided up into Qe and Qh based on the Bowen ratio)
Gapfilling method
  Relation between Penmen Monteith and Qe (Unclosed/Closed)
  Relation between Priestly Taylor and Qe (Unclosed/Closed)
  Gapfill Using REddyProc MDS method to gapfill Qe
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 13: Water Use Efficiency
GPP/ET
Data Types
Data Prep
Data Cleaning/Filtering
Data Checking
Footprinting
U*
Carbon
Energy
WUE

## Slide 14: Appendix 1:
Double coordinate rotations (this can vary depending on setup and site) (Tanner and Thurtell, 1969)
WPL Density correction (Webb et al., 1980)
Sensor Separation
Flagging policy (Foken, 2003)
Statistical analysis (typically leave as program (EddyPro) default) (Vickers and Mahrt, 1997)

## Slide 15: Appendix 2: Standardized Date Range
#Run this in R and it will send it to your clipboard, there it can be pasted into Excel. Needs modification for Mac.
StartTime=ISOdate(2020,01,01,0,0,0)
EndTime=ISOdate(2020,12,31,23,30,0)
TimeStamp=seq(StartTime, EndTime,by = '30 mins')
hh<- (as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%M"))/60)+as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%H"))
Year<-as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%Y"))
Month<-as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d",tz="GMT")) ,format = "%m"))
DoY<-as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%j"))
Hour<- as.numeric((as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%M"))/60)+as.numeric(format(as.POSIXct(strptime(TimeStamp,"%Y-%m-%d %H:%M",tz="GMT")) ,format = "%H")))
ts=data.frame(TimeStamp,Year,Month,DoY,Hour)
write.table(ts, file="clipboard-16384", sep="\t", row.names=FALSE)

## Slide 16: Appendix: 3
Raw fluxes were sampled at a frequency of 10 Hz, averaged over a half-hour, and the half-hour averages were saved on a CR1000 datalogger (Campbell Scientific, Logan, Utah, USA). All fluxes were corrected for density, sensor separation, time lag and coordinate rotation (double coordinate rotation was used) following common Fluxnet protocols (Webb et al., 1980; Kaimal and Finnigan, 1994; Leuning and Judd, 1996; Foken and Leclerc, 2004; Aubinet et al., 2012; Burba et al., 2012). The resulting half-hour fluxes were then processed in a custom R-Software script, which filtered each half-hour to ensure that it had at least 80% of the high-frequency records and that there was no potential for dew formation on the IRGA lenses by either precipitation or by comparing the dew point temperature to Ta. Additional filtering removed values that were greater than ±3 standard deviations of a moving average, which consisted of 10 half-hour neighbouring values; further filtering was completed to check for physically improbable values. The Kljun et al. (2015) footprint analysis was used to constrain the measured fluxes to be within 80% of the desired site boundaries, using their FFP R-functions. Thereafter, fluxes with a corresponding friction velocity (u*) of u* < 0.10 m s-1 were removed from the dataset. Following this, the filtered net ecosystem exchange (NEE) data was gap-filled and then partitioned into respiration (R) and gross primary productions (GPP) using the relationship between night-time respiration and Ta, following the methods and R-packages from Wutzler et al. (2018). The filtered energy fluxes were forced closed, with the additional energy partitioned based on the Bowen ratio (ß) (Wilson et al., 2002). ß is the ratio of sensible heat (Qh) to latent heat (Qe). For each available half-hour, Qe was gap-filled by scaling potential evapotranspiration, PET (Priestley and Taylor, 1972) to ET. The scaler (α) was calculated from the ratio between ET and PET. For periods where no α was available, the ratio was gap-filled using the MDS method outlined in Reichstein et al. (2005), where Q*, VPD, and u* were used as the gap-filling conditions; however, when this was not possible, the seasonal mean α was used. Qh was then gap-filled by solving the energy balance equation using the measured and gap-filled Q*, Qe and Qg.
References
Aubinet, M., Vesala, T., & Papale, D. (2012). Eddy covariance: a practical guide to measurement and data analysis. Springer & Business Media. Brown, S. M., Petrone, R. M., Mendoza, C., & Devito, K. J. (2010). Surface vegetation controls on evapotranspiration from a sub humid Western Boreal Plain wetland. Hydrological Processes, 24(8), 1072-1085. Falge, E., Baldocchi, D., Olson, R., & Anthoni, P. (2001). Gap filling strategies for defensible annual sums of net ecosystem exchange. Agric. For. Meteorol., 107, 43-69.Foken, T., & Leclerc, M. Y. (2004). Methods and limitations in validation of footprint models. Agriculture and Forest Meteorology, 127(3-4), 223-234. Kaimal, J. C., & Finnigan, J. J. (1994). Atmospheric boundary layer flows: their structure and management. New York: Oxford University Press. Kljun, N., Calanca, P., Rotach, M. W., & Schmid, H. P. (2015). A simple two-dimensional parameterisation for Flux Footprint Prediction (FFP). Geoscience Model Development, 8, 3695-3713. Oke, T. (1987). Boundary Layer Climates (Second ed.). New York: Methuen & Co Limited. Papale, D., Reichstein, M., Canfora, E., Aubinet, M., Bernhofer, C., Longdoz, B., . . . Yakir, D. (2006). Towards a more harmonized processing of eddy covariance CO2 fluxes: algorithms and uncertainty estimation. Biogeosciences Discussion, 3, 961-992. Petrone, R. M., Waddington, J. M., & Price, J. S. (2001). Ecosystem scale evapotranspiration and net CO2 exchange from a restored peatland. Hydrological Processes, 15(14), 2839-2845. Petrone, R., Chasmer, L., Hopkinson, C., Silins, U., Landhausser, S., Kljun, N., & Devito, K. (2015). Effects of harvesting and drought on CO2 and H2O fluxes in an aspen-dominated western boreal plain forest:early chronosequence recovery. Canadian Journal of Forest Research, 45(1), 87-100. Priestley, C. H., & Taylor, R. J. (1972). On the Assessment of Surface Heat Flux and Evaporation Using Large-Scale Parameters. Monthly Weather Review, 100(2), 81-92. Reichstein, M., Falge, E., Baldocchi, D., Papale, D., Aubinet, M., Berbigier, P., . . . Valentini, R. (2005). On the separation of net ecosystem exchange into assimilation and ecosystem respiration: review and improved algorithm. Global Change Biology, 11(9), 1424-1439. RStudio Team. (2016). RStudio: Integrated Development Environment for R. Bonston, MA: RStudio, Inc. Retrieved from http://www.rstudio.com/ Webb, E. K., Pearman, G. I., & Leuning, R. (1980). Correction of flux measurements for density effects due to heat and water vapour transfer. Royal Meteorological Society, 106(447), 85-100. Wilson, K., Goldstein, A., Falge, E., Aubinet, M., Baldocchi, D., Berbigier, P., . . . Verma, S. (2002). Energy balance closure at FLUXNET sites. Agricultural Forest Meteorology, 113, 223-243. Wutzler, Thomas, Antje Lucas-Moffat, Mirco Migliavacca, Jürgen Knauer, Kerstin Sickel, Ladislav Šigut, Olaf Menzer, and Markus Reichstein. "Basic and extensible post-processing of eddy covariance flux data with REddyProc." Biogeosciences 15, no. 16 (2018): 5015-503